## Slide 1: GET A GRIP ON SAFETY
Activity Package 6 – Safety Moment
Ladder Safety

## Slide 2: lAdder safety
Types of Ladders…
Extension Ladders
Step Ladders
Boarding Ladders
Fixed Ladders

## Slide 3: lADDER safety
How do we protect ourselves? Identify
Always make sure you use your ladder safely and follow these simple recommendations:
Always face the ladder when going up or down
When going up or down a ladder keep both hands free from tools, equipment or parts to ensure you maintain three-point contact
Only one worker should be on a ladder at any time
Look up/down before accessing a ladder
Portable ladders should be set up on a firm, level surface
To ensure you don't over-reach, keep the centre of your body within the side rails of the ladder

## Slide 4: lADDER safety
How do we protect ourselves?
Always make sure you use your ladder safely and follow these simple recommendations:
Don’t use makeshift items such as barrels or pails as a substitute for a ladder
Be very cautious getting on and off, or up and down, from equipment or facilities
When extended, the overlap of upper and lower sections must not be less than one metre
Secure the ladder at the top and bottom by tying it off or have another worker hold the ladder
Stepladders are not to be used as support for scaffold planks

## Slide 5: lADDER safety
How do we protect ourselves?
Always make sure you use your ladder safely and follow these simple recommendations:
Clean boots prior to using ladders
Use spike foot ladders for soft surfaces
Use non-slip foot ladders for hard, smooth surfaces
Use nonconductive ladders for electrical work
Take personal responsibility. Understand and mitigate the hazards around you and your co-workers.

## Slide 6: Ladder SAFETY